## Slide 1: CODA Online Data Formats
Mar 26, 2025

## Slide 2
Key to Reading Data Layouts
1, 32-bit item
Additional, unnamed items of type immediately above
Evio container of type bank, segment, or tagsegment
item3
item4
…
Item 2
Item 1
MSB (31) LSB(0)
8 bits 16 bits
1, 64-bit item: If big endian, Lower memory has most significant 32 bits. Opposite for little endian.
Increasing Memory
Increasing Memory, BIG endian
Increasing Memory, LITTLE endian

## Slide 3
Bank :
Length (32 bit words, exclusive)
Tag (16 bits) (2) Type (6) Num (8)
32 bits
Padding
Evio Header Formats
Segment :
Tag (8 bits) (2) Type (6) Length (16)
Padding
Tag Segment :
Tag (12 bits) Type (4) Length (16)
MSB (31) LSB (0)
Number of unused bytes at end of following data if not a multiple of 32 bits.
For shorts, it is 0 or 2.
For chars (not strings), it is 0, 1, 2, or 3

## Slide 4
Evio Content Type Codes
Content Type | Primitive Data Type | Content Type | Primitive Data Type
0x0 | 32 bit unknown (not swapped) | 0x21 | Hollerit (Composite data internal)
0x1 | 32 bit unsigned int | 0x22 | N value (32 bit int, Composite data internal)
0x2 | 32 bit float | 0x23 | n value (16 bit int, Composite data internal)
0x3 | 8 bit char* (string) | 0x24 | m value (8 bit int, Composite data internal)
0x4 | 16 bit signed int |  | 
0x5 | 16 bit unsigned int |  | 
0x6 | 8 bit signed int |  | 
0x7 | 8 bit unsigned int |  | 
0x8 | 64 bit double |  | 
0x9 | 64 bit signed int |  | 
0xa | 64 bit unsigned int |  | 
0xb | 32 bit signed int |  | 
0xc | Tag Segment |  | 
0xd | Segment |  | 
0xe | Bank |  | 
0xf | Composite |  | 
0x10 | Bank |  | 
0x20 | Segment |  | 

## Slide 5
tag ¦ type ¦ length
data format string ...
length
tag ¦ pad ¦ type ¦ num
actual data ...
Composite Data Type
32 bits
MSB (31) LSB (0)
In Hall B’s new data type, the first word comprises a TAGSEGMENT header which is followed by a string describing the data to come. After this TAGSEGMENT containing the data format string, is a BANK containing the actual data.

## Slide 6
Block Header (evio format versions 1-3)
1 | Block Length
2 | Block Number
3 | Header Length
4 | Start
5 | End
6 | Version
7 | Reserved
8 | Magic Number
Length of block in 32-bit words, inclusive
Record id starting at 0
Length of block header in 32-bit words (8)
Offset in words to first event header in block relative to start of block
Number of valid words in block (header + data). Same as block length except for the last block.
Evio format version
Reserved
Number for endianness tracking (0xc0da0100)

## Slide 7
Block Header (evio format version 4)
1 | Block Length | 
2 | Block Number | 
3 | Header Length | 
4 | Event Count | 
5 | Reserved 1 | 
6 | Bit Info | Version
7 | Reserved 2 | 
8 | Magic Number | 
Length of block in 32-bit words, inclusive
Order of block in network transfer (record id) starting at 1. From ROC: -1 if payload banks not being built.
Length of block header in 32-bit words (8)
Number of evio events (payload banks) in block, not including dictionary.
If content is being built (eg ROC Raw type), = source CODA id, else reserved
Evio format version in low 8 bits. Bit Info in high 24 bits See next slide.
Reserved
Number for endianness tracking (0xc0da0100)

## Slide 8
Block Header, Bit Info / Version Word
Evio Version
Data Info
Reserved
15 - 8
7 - 0
BIT | FUNCTION (if bit set)
8 | Dictionary exists
9 | Is last record in stream or file
10-13 | Data content type for CODA online only: ROC Raw = 0, Physics = 1, Partial Physics = 2, Disentangled = 3, User = 4, Control = 5, Mixed = 6, Other = 15
14 | Has ”first event” (in every split file) which is first USER type event in this block
15 | Streaming data (not triggered)
16-31 | Reserved
NOTE: User events from ROC are typed as ROC Raw (EB handles this).

## Slide 9
HIPO/EVIO FORMAT VERSION 6

## Slide 10
Record
Uncompressed
Compressed
Record Header
Index Array of Event Lengths (bytes, one word per length)
User Header
Pad 1
Events
Pad 2
Record Header
Compressed Data
Pad 3

## Slide 11
Evio Events
HIPO Events
Event 1
Event 2
Event N
Pad 2
…
Event 1
Event 2
…
Event N

## Slide 12
File Trailer
Record Header
Optional Uncompressed Array: record (not event !) length in bytes, followed by its event count
(2 words / record)
(all records except this trailer)

## Slide 13
Record Header
1 | Record Length |  | 
2 | Record Number |  | 
3 | Header Length |  | 
4 | Event Index Count |  | 
5 | Index Array Length |  | 
6 | Bit Info |  | Version
7 | User Header Length |  | 
8 | Magic Number |  | 
9 | Uncompressed Data Length |  | 
10 | Type | Compressed Data Length | 
11 12 | User Register 1 |  | 
13 14 | User Register 2 |  | 
Length of record in 32-bit words, inclusive. If compressed, it’s the length of compressed data (including pad 3) + length of this header.
Record id from 1. From ROC: -1 if payload banks not being built
Length of this header in 32-bit words (always 14)
Number of events contained (Evio: not including dictionary). Same as index array length in 32-bit words if array exists.
Length of index array in bytes. Each array word is an event length in bytes.
Evio format version in low 8 bits. Bit Info in high 24 bits
Optional user header length in bytes
Number for endianness tracking (0xc0da0100)
Length of uncompressed index + user header + events in bytes. Does not include padding (pad 2).
Compression type in high 4 bits (0=none, 1 = LZ4, 2 = LZ4 Best, 3 = GZIP). Length of compressed data (index + user header + events) in 32-bit words (low 28 bits) which includes padding (pad 3) to 4 byte boundary .
User defined long word (64 bits)
User defined long word (64 bits)

## Slide 14
File/Record Headers, Bit Info / Version Word
Evio Version
Data Info
Padding Info
General Header Type
Reserved
21, 20
23, 22
25, 24
31 - 28
27, 26
19 - 8
7 - 0
Value | Header Type
0 | Evio record
1 | Evio file
2 | Evio extended file
3 | Evio file trailer
4 | HIPO record
5 | HIPO file
6 | HIPO extended file
7 | HIPO file trailer
Bits | Padding
25-24 | Pad 3
23-22 | Pad 2
21-20 | Pad 1
Bit uses depend on header type

## Slide 15
Data Info Bits for Headers
BIT (from 0) | RECORD HEADER (if bit on)
8 | Dictionary exists (first record only)
9 | Is last record in stream or file
10-13 | Data content type for CODA online only: ROC Raw = 0, Physics = 1, Partial Physics = 2, Disentangled = 3, User = 4, Control = 5, Mixed = 6, ROC Raw Streaming = 8, Physics streaming = 9, Other = 15
14 | Has “first event” (first record only, in every split file)
15-19 | Reserved
BIT (from 0) | FILE HEADER (if bit on)
8 | Dictionary exists
9 | Has “first event” (in every split file)
10 | File trailer with index array exists
11-19 | Reserved

## Slide 16
File
Data Record 1
Data Record N
File Header
Index Array*
User Header
Pad 1
* Same format as file trailer index:
1 word (4 byte int) of byte length, followed by 1 word of event count,
for each record (not event!)

## Slide 17
File Header
1 | ID | 
2 | File Number | 
3 | Header Length | 
4 | Record Count | 
5 | Index Array Length | 
6 | Bit Info | Version
7 | User Header Length | 
8 | Magic Number | 
9 10 | User Register | 
11 12 | Trailer Position | 
13 | User Integer 1 | 
14 | User Integer 2 | 
Identification word. For Evio = 0x4556494F (EVIO in ascii). For HIPO = 0x43455248 (CERH in ascii).
If file being split, the split number (starting at 1)
Length of this header in 32-bit words (always 14)
Number of records contained. Same as index array length in 32-bit words if array exists.
Length of index array in bytes
Evio format version in low 8 bits. Bit Info in high 24 bits
Optional user header length in bytes
Number for endianness tracking (0xc0da0100)
64 bit register available for user
Number of bytes from beginning of file to beginning of trailer (ending general record header). Value of 0 means either no trailer exists or its position is unavailable
Integer available for user
Integer available for user

## Slide 18
EXTENDED File Header
(Differences)
3 | Header Length
15 + | User Integers 3+
Length of this header in 32-bit words GREATER THAN 14
Additional integers available for user beyond the regular general file header.

## Slide 19
Network Transfer (Evio 4 Output) Format
Number of 32-bit words in evio block, inclusive.
Each payload bank can be a Physics Event, ROC Raw Record, Control Event, or User event. Note: there may be a block header between any 2 payload banks.
Format used when sending all types of online CODA data over the network. They are in standard evio buffer/file output format with block headers.
Block Length
Event Count
Header Length = 8
Reserved 1
Payload Bank
Payload Bank
Evio Block Header
Payload Banks
Payload Bank
Block Number
Reserved 2
Bit Info Version
Magic Number
Normally order of block in the file/network transfer & starts at 1. If sent by ROC , = -1 if payload banks not being built, else record id.
Length of block header in 32-bit words.
Number of evio events (payload banks) in block, not including dictionary.
If content type is being built (eg ROC Raw), = source CODA id,
else reserved.
Version: lowest 8 bits (Bits 0-7).
Bit Info: Bit 8 = has dictionary, Bit 9 = is last block,
Bits 10-13 = payload bank type (ROC Raw = 0, Physics = 1,
PartialPhysics = 2, Disentangled = 3, User = 4,
Control = 5, Mixed = 6, ROC raw streaming = 8, Physics streaming = 9, Other = 15).
Bit 14 = has “first event” (in every split file) is first USER type
event in this block
NOTE: User events from ROC are typed as ROC Raw (EB handles this).
Reserved.
Magic Number (0xc0da0100) for endianness tracking.

## Slide 20
Control Event
Control Event Length = 4
time
Header
B
Bank of uints
16 bit Control event type:
0xFFD0, Sync
0xFFD1, Prestart
0xFFD2, Go
0xFFD3, Pause
0xFFD4, End
Event Type 0x01 0
Event Type 0x01 0
A
Event Type | A | B
Sync | # events since last sync | # events in run
Prestart | run number | run type
Go | (reserved) | # events (or frames if streaming) in run so far*
Pause | (reserved) | # events (or frames if streaming) in run so far*
End | (reserved) | # events (or frames if streaming) in run so far*
*Control events included in event count but not in frame count

## Slide 21
ROC Raw Data Record
Each data block has M events. There are multiple blocks only if multiple DMAs used in data collection. See Data Block Bank diagram.
Bank of banks
Number of events. If = 0, indicates a User event from ROC.
4 bit Status
12 bit ROC ID (0 - 255)
Low 32 bits of event number used for building, starting at 1 (EB uses 64-bit value). 48-bit (max) timestamp for building is written as 2, 32-bit ints (low 32 first, high 16 last regardless of endian). Ts & misc. data are optional, but events from a particular run must have same type and number of data.
S ROC ID 0x10 M
Unused
Big Endian
Error
Sync
BE ER SY
Header
Trigger Bank
Bank type = 0XFF10 if no timestamps, see following chart
Bank of segments
Number of events
0xFF1X 0x20 M
Event ID or Trigger Type
Segment of 32 bit ints
Length of segment
ID M 0x01 ID Len M
Data Banks
Record Length
Trigger Bank Length
Data Block Bank 1
Data Block Bank Last
(One segment for each event)
S ROC ID 0x10 M
0xFF1X 0x20 M
Event Number 1
Timestamp1 (31 – 0)
Misc. 1 (?)
ID 1 0x01 ID Len 1
…
Timestamp1 (47 – 32)
Event Number M
Timestamp M
Misc. M (?)
ID M 0x01 ID Len M

## Slide 22
ROC Time Slice Bank
Header
Stream Info
Bank
(SIB)
Data Banks
ROC Bank Length
Stream Info Length
PP 1 Data
ROC ID 0x10 SS
0xFF30 0x20 SS
…
Frame Number
Timestamp1 (31 – 0)
0x31 0x01 TSS Len
Timestamp1 (63 – 32)
Bank of banks
Stream Status
16 bit ROC ID
ROC ID 0x10 SS
Err Total Streams Stream Mask
6 - 4
3 - 0
Payload 2 Payload 1
… …
0x41 0x85 AIS Len
0 Payload N
Payload Port 1 Length
PP 1 ID 0x0 SS
Payload Port N Length
PP N ID 0x0 SS
PP N Data
Time Slice Segment (TSS)
2nd byte: top 2 bits = 2 for padding if odd # payloads (else 0), lower 6 bits is type 5 (unsigned short) => 0x85 (1000 0101)
Bits 7
Payload Port (SS) : 7 6-3 2 1 0
Err Mode DD ND
ND = No Data Available DD = Data was Discarded
Aggregation Info Segment (AIS)
Err ND DD Module ID Bond? Lane ID Payload Port #
4 - 0
7
11 - 8
6 , 5
15 14 13 12

## Slide 23
Header
ROC Time Slice Banks
Aggregated Bank Length
0xFF60 0x10 SS
Bank of banks
Built Physics for Streaming
0xFF60 0x10 SS
Streaming Physics Event
ROC N Time Slice Bank
ROC 1a TS Bank Len
…
ROC 2 Time Slice Bank
ROC 1b Time Slice Bank
Stream Info Bank Length
0xFF31 0x20 SS
Stream Info
Bank (SIB)
Frame Number
Avg Timestamp (31 – 0)
0x32 0x01 TSS Len
Avg Timestamp (63 – 32)
ROC 1
ROC 2 …
0x42 0x01 AIS Len
ROC N
Time Slice Segment (TSS)
ROC ID 0x10 SS
ROC 1 Data
Stream Status
Err Total Streams
Bit 7
6 - 0
Aggregation Info Segment (AIS)
SS1 = duplication of SS from ROC (blank if frame missing)
SS2 = For missing frames, Err = 1 and Reserved holds low 7 bits of missing frame counter,
bits: 15 14-8
ROC ID SS2 SS1
7 - 0
15 - 8
Bits 31-16
Err Reserved
TS Banks: Multiple time slices can be transported as defined in EVIO header. Multiple streams can be included as defined by Stream Status bits.

## Slide 24
Header
Aggregated Bank Length
0xFF68 0x10 SS
Bank of banks
Built Physics for Streaming
0xFF68 0x10 SS
Streaming Physics Event Empty Frame
Stream Info Bank Length
0xFF32 0x20 SS
Stream Info
Bank (SIB)
Frame Number
Est Timestamp (31 – 0)
0x32 0x01 TSS Len
Est Timestamp (63 – 32)
ROC 1
ROC 2 …
0x42 0x01 AIS Len
ROC N
Time Slice Segment (TSS)
Stream Status
1 Total Streams
Bit 7 Err
6 - 0
Aggregation Info Segment (AIS)
SS2:
ROC ID SS2 0
7 - 0
15 - 8
Bits 31-16
1 low 7 bits of missing frame counter

## Slide 25
Header
Time Info
Bank (TIB)
ROC Time Slice Banks
Physics Event Length
0xFF6X 0x10 TC
Time Info Bank Length
0xFF31 0x01 TC
Avg. Timestamp1 (31 – 0)
Avg. Timestamp1 (63 – 32)
Frame Number
Bank of banks
Built Physics for Streaming
0xFF6X 0x10 TC
ROC TSB Count
Note: there can be up to 4 streams from each ROC
Streaming Physics Event (OLD)
ROC N Time Slice Bank
ROC 1a Time Slice Bank
…
ROC 2 Time Slice Bank
ROC 1b Time Slice Bank

## Slide 26
TRIGGER BANK TAGS
Tag Value | Purpose
0xFF10 | Raw trigger, no timestamps
0xFF11 | Raw trigger, w/ timestamps
0xFF20 | Built trigger, no timestamps, no run # & run type, includes run specific data
0xFF21 | Built trigger, w/ timestamps, but no run # & run type, includes run specific data
0xFF22 | Built trigger w/ run # & run type, but no timestamps, includes run specific data
0xFF23 | Built trigger with timestamps and run # & run type, includes run specific data
0xFF24 | Built trigger, no timestamps, no run # & run type, no run specific data
0xFF25 | Built trigger, w/ timestamps, but no run # & run type, no run specific data
0xFF26 | Built trigger w/ run # & run type, but no timestamps, no run specific data
0xFF27 | Built trigger with timestamps and run # & run type, no run specific data
0xFF4F | Built trigger using at least one ROC with bad or nonexistent trigger bank

## Slide 27
PHYSICS EVENT TAGS
Tag Value | Purpose
0xFF50 | Event built by primary event builder
0xFF58 | Event built by primary event builder with sync bit set
0xFF70 | Event built by secondary event builder
0xFF78 | Event built by secondary event builder with sync bit set

## Slide 28
STREAMING TAGS
Tag Value | Purpose
0xFF30 | Stream Info Bank (SIB) from ROC containing frame # followed by timestamp
0xFF31 | Stream Info Bank (SIB) from Aggregator containing frame # followed by timestamp
0xFF32 | Stream Info Bank (SIB) from Aggregator containing frame # followed by timestamp with non-fatal error
0x31 | Time Slice Segment (TSS) from ROC containing frame # followed by timestamp
0x41 | Aggregation Info Segment (AIS) from ROC
0x32 | Time Slice Segment (TSS) from Aggregator containing frame # followed by timestamp
0x42 | Aggregation Info Segment (AIS) from Aggregator
0xFF60 | Built from ROC Raw Data streamed from ROC / VTP
0xFF61 | Built from ROC Raw Data streamed from ROC / VTP with non-fatal error
0xFF62 | Possibly: event built by DC event builder in streaming mode
0xFF64 | Possibly: event built by secondary event builder in streaming mode
0xFF66 | Possibly: event built by primary event builder in streaming mode
0xFF68 | Missing Frame (no ROC data available, estimate for timestamp)

## Slide 29
CODA RESERVED
BANK TAGS
Tag Value Range | Purpose
0xFF00 - 0xFFFF | Complete range of reserved values
0xFFE0 - 0xFFFF | Undetermined
0xFFD0 - 0xFFDF | Control events
0xFF90 - 0xFFCF | Undetermined
0xFF50 - 0xFF8F | Physics events
0xFF10 - 0xFF4F | Trigger banks
0xFF00 - 0xFF0F | Undetermined
CONTROL EVENT TAGS
Tag Value | Control Event
0xFFD0 | Sync
0xFFD1 | Prestart
0xFFD2 | Go
0xFFD3 | Pause
0xFFD4 | End
PHYSICS EVENT TAGS
Tag Value | Event Made by
0xFF50 | PEB
0xFF58 | PEB with sync set
0xFF70 | SEB
0xFF78 | SEB with sync set
0xFF60 | Streaming ROC Raw
0xFF62 | Streaming DC
0xFF64 | Streaming SEB
0xFF66 | Streaming PEB
4th bit set indicates that the last event in the entangled block is a sync event

## Slide 30
Partially-Built Physics Event (Data Concentrator Output)
Each data bank wraps 1 or more data blocks from a ROC.
One bank for each ROC. See Data Bank diagram.
Bank type: see Trigger Bank Tags table
Bank of segments
Number of ROCs
Common or ROC Segments
Optional: These segments will not exist if trigger data is sparsified or built in single event mode. See Trigger Bank Tags table & Built Trigger Bank diagram.
Physics Event Length
Built Trigger Bank Length
Data Bank 1
…
Header
Built Trigger Bank
Data Banks
ROC 1 Segment
ROC N Segment
2 Common (EB) Segments
Data Bank N
…
Bank of banks
Number of events
4 bit Status
12 bit Event Builder ID
S EB ID 0x10 M
Unused
Big Endian
Error
Sync
BE ER SY
S EB ID 0x10 M
0xFF2X 0x20 N
0xFF2X 0x20 N

## Slide 31
Physics Event’s Built Trigger Bank
Common Data
ROC
Data
Array containing type (trigger ID) of each event.
ROC ID
Segment of ints
Len of segment
Optional: ROC specific metadata starting with timestamp (low 32 first). If sparsify config flag set, and no metadata exists, or if built in single event mode, there is no segment.
roc id 0x01 Len
ID of EB that built this bank (8bits)
Segment of unsigned shorts (6 bits)
Len of seg
EB id p 5 Len
Header
ID of EB that built this bank
Segment of 64 bit uints
Len of segment
EB id 0xa Len
64 bit number of first event in physics bank.
Built Trigger Bank Length
0XFF2X 0x20 N
…
EB id p 5 Len
Event Type 2 Event Type 1
Event Type M Event Type M-1
Timestamp for event 1
Misc. for event 1
roc1 id 0x01 Len
…
Timestamp for event M
Misc. for event M
Run Number & Run Type
EB id 0xa Len
First Event Number
Average Timestamp 1
…
Average Timestamp M
Optional: Timestamps. If checking consistency, the avg. timestamp of all ROCs for each.
Optional: run # in high 32 bits. Run type in low 32 bits.
Padding (2bits)
(one for each ROC, to ROC N)

## Slide 32
Physics Event
Each data bank wraps 1 or more data blocks from a ROC.
One bank for each ROC. See Data Bank diagram.
Bank type: see Trigger Bank Tags table
Bank of segments
Number of ROCs
Physics Event Length
Built Trigger Bank Length
Data Bank 1 for ROC 1
…
Header
Built Trigger Bank
Data Banks
ROC 1 Segment
ROC N Segment
2 Common (EB) Segments
Data Bank N for ROC N
…
Bank of banks
Number of events
12 bit Event Builder ID:
see Physics Event Tags table
0xFFXX 0x10 M
0xFFXX 0x10 M
0xFF2X 0x20 N
0xFF2X 0x20 N
Common or ROC Segments
Optional: These segments will not exist if trigger data is sparsified or built in single event mode. See Trigger Bank Tags table & Built Trigger Bank diagram.

## Slide 33
Physics Event’s Data Bank
Data Bank Length
Data Block Bank 1
…
Bank of banks
Number of events
12 bit ROC ID
(Same 2nd header word as used in ROC Raw Record.)
Data Block Bank Last
Data blocks from a single ROC are wrapped in this data bank. There should be at least one data block and there may be more if more than one DMA is used in acquiring data for this ROC. If more than one block, each contains a fragment for every one of the M events and from unique modules. In addition, the last block may have data associated only with the last event (such as scalar data).
4 bit status
S ROC id 0x10 M
S ROC id 0x10 M
See Data Block Bank diagram.
Header

## Slide 34
Data Block Bank
Data Block Bank Length
Starting Event Number
Bank of ints
If single event mode,
E = event type
else,
E = number of events
12 bit Description
Raw Data
S D 0x01 E
S D 0x01 E
Single event mode
Big Endian
Error
Sync
SE BE ER SY
Header
Contains raw data from a single ROC containing one or more events. If this block is the last in a data bank, and there are multiple events, and E = 1, then this data is associated only with the last event (e.g. scalar readout).
Timestamp
Low 32 bits
Raw data may be an int array or it may contain evio bank structures.
4 bit status
detector ID
12 bit detector ID

## Slide 35
16-bit EVIO CODA-Format Tag
12 bits of identification which have:
  ROC ID for ROC Raw Records and Data Banks
  EB ID for partially built Physics Events
4 bits which can be:
  Status bits for ROC Raw Records, partially built Physics Events, and Data Banks:
    4th (MSB) – Unused (previously single event mode)
    3rd – Big endian data (data is unswapped )
    2nd - Error
    1st (LSB) – Sync
S ID
16 bits of identification which are: 0xFF00 – 0xFFFF in physics event and trigger bank tags. Refer to table.

## Slide 36
Disentangling Built Physics Event

## Slide 37
Physics
Event
Trigger Bank
Event Length
ROC 1 Data Bank
…
ROC N Data Bank
Data
Bank
Bank Length
Data Block Bank 1
…
Data Block Bank Last
Data
Block
Bank
Block Len
Start Ev Num
Raw Data
M
ROC 1
Raw Data
(FADC 250)
…
Block Header
…
Event Header 1
Raw Data 1 …
Event Header M
Raw Data M …
Block Trailer
Module 1
Block Header
…
Event Header 1
Raw Data 1 …
Event Header M
Raw Data M …
Block Trailer
Module K
One data block for each DMA in a single ROC. Each block must read out unique modules and in the same manner. In single event mode, only one block exists.
Entangled Data Format
Last block may have data associated only with last event.

## Slide 38
…
Block Header
…
Event Header 1
Raw Data 1 …
Event Header M
Raw Data M …
Block Trailer
Block Header
…
Event Header 1
Raw Data 1 …
Event Header M
Raw Data M …
Block Trailer
ROC 1
Raw Data
…
Block Header
…
Event Header 1
Raw Data 1 …
Event Header M
Raw Data M …
Block Trailer
Block Header
…
Event Header 1
Raw Data 1 …
Event Header M
Raw Data M …
Block Trailer
Module 2
…
Block Header
…
Event Header 1
Raw Data 1 …
Event Header M
Raw Data M …
Block Trailer
Block Header
…
Event Header 1
Raw Data 1 …
Event Header M
Raw Data M …
Block Trailer
ROC 2
Raw Data
Event 1 Raw Data
ROC 1
ROC 2
Entangled To Disentangled FADC 250 Raw Data
Data block bank 1
Data block bank 2
Module 1
ROC 2 Bank Header
Module 1 Event Header
Raw Data …
Module 2 Event Header
Raw data …
…
ROC 1 Bank Header
Module 1 Event Header
Raw Data …
Module 2 Event Header
Raw data …
Module J Event Header
Raw Data …
Module K Event Header
Raw Data …
…

## Slide 39
Disentangled Physics Event
Each data bank wraps raw data from all ROCs.
See Single Event Data Bank diagram.
Physics Event Length
Event 1 Data Bank
…
Header
Data Banks
Event M Data Bank
Bank of banks
Number of events
4 bit Status
Number of ROCs
S N 0x10 M
Single event mode
Big Endian
Error
Sync
SE R ER SY
S N 0x10 M

## Slide 40
Single Event (Disentangled) Data Bank
Bank of banks
# ROCs
Disentangled Data Bank
4 bit status
S 0xFF30 0x10 N
4 bit Status
Single event mode
Big Endian
Error
Sync
SE R ER SY
Header
ROC N
Data Block Bank Length
S 0xFF30 0x10 N
…
ROC 1
ROC N Bank Length
Module 1 Event Header
Raw Data …
Module K Event Header
Raw Data …
…
Non-Module Event Header
Raw Data …
Some Rocs, on the last event of a block of events, may have non-module data (e.g. scalar data).
(one for each ROC)
ROC 1 Bank Length
0 6 0x01 KK
1 6 0x01 K
…
Event Number (63 - 32)
Event Number (31 – 0)
Timestamp (47 – 32)
Timestamp (31 – 0)
Event Type (15 – 0)
Run Number
64 bit event #, 48 bit mean timestamp, 16 bit event type and 32 bit run number of this event.
Bank of ints
Number of modules
Number of words before module data
1 6 0x01 K
1 in high bit if have non-module data

## Slide 41
31st bit | Bits | Usage
1 | 30 - 27 | 4-bit data type (see chart)
1 | 26 - 0 | Data type dependent data payload
0 | 3 0 - 0 | Data payload using last defined data type
Data Type Values | 
0 – block header 1 – block trailer 2 – event header 3 – trigger time 4 – window raw data 5 – window sum 6 – pulse raw data | 7 – pulse integral 8 – pulse time 9 – streaming raw data 10 – 12 user defined 13 – event trailer (debug only) 14 – data not valid (empty module) 15 – filler (non-data) word
Block Trailer Word Format
Bits | Value | Comment
31 | 1 | This is a type defining word
30 – 27 | 1 | Data type = block trailer
26 – 22 | Slot ID | Set by VME64 backplane
21 – 0 | Total # of words in block of events | Number of 32 bit words in block
Block Header Word Format
Bits | Value | Comment
31 | 1 | This is a type defining word
30 – 27 | 0 | Data type = block header
26 – 22 | Slot ID | Set by VME64 backplane
21 – 14 | Event # | Number of events in block
13 – 12 | Module Type | 0=FADC250, etc.
11 – 0 | Event block # | Used to align block when building events
Event Header Word Format
General Data Word Format
FADC 250
Bits | Value | Comment
31 | 1 | This is a type defining word
30 – 27 | 2 | Data type = event header
26 – 22 | Slot ID | Set by VME64 backplane
21 – 20 | Module type | 0=FADC250, etc.
19 – 0 | Trigger number | ADC processing chip #

## Slide 42
Streaming Format proposed by
Graham Heyes
Uncompressed
Payload Length
Compressed
Payload Length
Source ID
Magic Number
Data Compressed
Data Uncompressed
Total Len (bytes)
Compressed Len (bytes)
Format Version
Timestamp (128 bit) =
Seconds (64 bits)
Nanoseconds (64 bits)
Payload Len (bytes)
Record Count (64 bit)
Padding
Total Length
MSB (31) LSB(0)
Increasing Memory
Increasing Memory, BIG endian
Increasing Memory, LITTLE endian
First to simplify routing
Filter out rogue connections, endian considerations

## Slide 43
Possible Streaming Format
Payload Length
Compression type,
Source type,
Data structure,
…
Magic Number
Format Version
Data Compressed
Data Uncompressed
Source ID
Timestamp (128 bit)
Record Count (64 bit)
Padding
Total Length
Total Length (bytes)
Payload Length
Compressed Length
Bit Info
Compressed
Payload Length